## Slide 1: Great Lakes Water Levels and Coastal Systems
Coastal Resiliency and Climate Change
Scudder D. Mackey, Ph.D.
Ohio Department of Natural Resources
Lake Erie Millennium Conference
October 30, 2013

## Slide 2: What Drives Water Level Change?
Climate
  Precipitation + Runoff – Evaporation = NBS
Seasonal changes in climate (annual)
Inflows and Outflows
  Connecting Channel Flows between Lakes
  Water-Level Regulation
Diversions (into and out of basin)
Consumptive Uses
Wind and Storm Events (short term)

## Slide 3
Basinwide Drop in
GL Water Levels

## Slide 4
August 2013 Forecast

## Slide 5: Climate Variability and Water Levels
According to the most recent climate models, climate change in the Great Lakes basin during the next 30-70 years is likely to be characterized by:
  Increase in storm severity - an increase in precipitation and more frequent and intense storms (weather variability);
  Increase in evaporation - an increase in lake evaporation resulting from higher surface water temperatures, increased wind speed, lack of winter ice;
  Change in seasonal timing - increased water supply during winter/spring months (increased precipitation) accompanied by larger decreases in supply during summer/fall months (increased evaporation) resulting in slight overall annual declines in Great Lakes water levels.
Notes: We've used two types of climate models in our studies - the global climate models, and the more localized Regional Climate models, adapted to the Hydroclimatology of the Great lakes.
The GCMs generally show the following characteristics a much wider range of low and high water levels. Overall, the RCMs predict that NBS will be near historic norms - certainly well within the band of paleo-climate excursions.
5

## Slide 6: Future Lake Erie Water Levels
Lake Erie water levels are anticipated to remain below long-term historic mean water levels, but generally within the range of historic water levels.
  Anticipate more extreme and variable water level events, i.e. anticipate water level regimes that may exceed historic thresholds, both low and high.
How might these changes impact the Lake Erie coast and shorelines?
How vulnerable is our coast to these stressors?
What can we do to adapt to minimize the impact of environmental and socio-economic climate stressors?

## Slide 7: Changes in Water Level Regime
Major shifts in shoreline position/location
Loss of hydraulic connectivity
  Wetlands
  Small tributaries
  Loss of wetlands and fish spawning/nursery habitat
Changes in seasonal magnitude, timing and duration
  Seasonal highs and lows
  Intermittently exposed Western Basin reefs (Lake Erie)?
Altered tributary flows and Lake circulation patterns
  Connectivity between spawning and nursery habitats
  Nutrient and contaminant loadings
  Altered littoral sediment transport rates (nearshore habitat)

## Slide 8: Coastal Habitat Enhancement Initiative
Collaborative effort between the Ohio Division of Wildlife, University of Toledo, Ohio EPA, and ODNR Office of Coastal Management
Shoreline alteration affects fish species diversity and abundance
Armoring alters diversity but response is variable based on underlying substrate/habitat types
Shoreline/terrestrial vegetation positive effect
Develop habitat use index and develop model to simulate future shoreline conditions
Stratify management goals based on shoreline types

## Slide 9: Coastal Habitat Outreach, Education, Implementation and Research
Habitat Enhancement Flyer
  Background
  Results
  Suggested Actions
  Fish Photos/Community Groupings
  Importance (GL Fishery, Benefits)
Develop Habitat Enhancement Guidance
  Distribution at pre-application site visits (OCM)
  Incorporation into reach-based LESEMP (OCM)
  Incorporation into Coastal Design Manual (OCM)

## Slide 10: Sand Resource Management
Collaborative effort between the Ohio Division of Geological Survey and ODNR Office of Coastal Management
Calculate volume of coarse-grained sediment contributed to the littoral zone by bluff erosion.
Volume is annualized and expressed as cubic yards/year. Surrogate for net sediment transport rate.
Can be used to quantify cumulative impacts of shore protection on sand resources and nearshore habitat.

## Slide 12: Superstorm Sandy (1-year Anniversary)
Impacts of Superstorm Sandy included sand transport landward.
  Increase in beach widths
  Navigation channels blocked by sand
Massive dredging effort spring 2013 a result of low Lake Erie water levels and littoral sand transport by Sandy.
Nearshore habitat impacts are unknown. Limited baseline data. Change detection not possible.

## Slide 13: Vulnerability Assessment and Thresholds for Restoration Projects
Objective is to identify water-level ranges and thresholds that minimize adverse impacts to restoration projects and provide a mechanism to anticipate potential impacts due to changing water level regimes.
What parameters are required for your restoration project function successfully?
  What are the thresholds beyond which your project will be severely compromised and eventually fail?
  Is it plausible that those thresholds will be reached or surpassed?
  If so, can you modify the design such that functionality is maintained or enhanced?
  If not, are there alternative functional benefits that would accrue under a different set of conditions? (e.g. fish habitat converts to wetland habitat)
Notes: Vulnerability and Threshold concepts…

## Slide 14: How High is “High” and how Low is “Low”?
1969 - 1998
1933 - 1945
568.2 (1934)
574.3 (1986)
575.5
1.2 ft
567.3
0.9 ft
571.3 (mean)

## Slide 15: Summary
Lake Erie water levels are anticipated to remain below long-term historic mean water levels, but generally within the range of historic water levels.
  Anticipate more extreme and variable water level events, i.e. anticipate water level regimes that may exceed historic thresholds, both low and high.
Areas for future research/data needs:
  Future water level regimes (maximum and minimum values, duration)
  Nearshore habitat enhancements (biotic and abiotic linkages)
    Bathymetry, substrate, shoreline condition assessments
    Nearshore aquatic communities, habitat linkages
  Sand resource management (environmental and economic impacts)
    Distribution, source areas, littoral sediment transport rates and direction
  Low and High Water Thresholds (magnitude and duration)
    Ecological impacts, design criteria for restoration and enhancement projects
  Nearshore and Coastal Vulnerability Assessments
    Climate change and water level regime scenarios

## Slide 17: Lake Erie Bathymetry
Central Basin
Eastern Basin
Western Basin
Lake
St. Clair

## Slide 18: Hydrological Components
Lake Superior
Hydrologic Values 1948-2006
Courtesy IUGLS
Long Lac/ Ogoki
154 m3/s (5400 cfs).
Chicago Diversion
91 m3/s (3,200 cfs)
Lake Michigan-Huron
Lake Erie
56% precipitation
40% runoff
4% diversions
----------------------
43% evaporation
57% outflow
39% precipitation
34% runoff
27% inflow
----------------------
31% evaporation
68% outflow
1% Chicago diversion
79% inflow
11% precipitation
10% runoff
----------------------
89% outflow
11% evaporation
Lake Superior
Lake Ontario
79% inflow
15% runoff
6% precipitation
----------------------
93% outflow
7% evaporation
St. Marys River
2110 m3/s
St. Clair/Detroit River
5360 m3/s (190,000 cfs)
Niagara River
5780 m3/s (204,000cfs)
St. Lawrence
7060 m3/s

## Slide 19: Diversions and Impacts
Lake Superior
Great Lakes
Courtesy IUGLS
Long Lac/ Ogoki
154 m3/s (5,400 cfs).
Chicago Diversion
91 m3/s (3,200 cfs)
Welland Canal
244 m3/s (8620 cfs)
+9 cm (+3.5”)
0
0
Net +9 cm (+3.5”)
+7 cm (+2.8”)
-4 cm (-1.6”)
-12 cm (-4.7”)
Net -9 cm (-3.5”)
+11 cm (+4.3”)
-6 cm (-2.4”)
-4 cm (-1.6”)
Net +1 cm (+0.4”)
Lake Michigan-Huron
Lake Erie
Connecting Channel
Diversion in
Diversion out
Diversion within
St. Clair River
Sault St. Marie
Control Structures
Cornwall Massena
Control Structures

## Slide 20
August 2013 Forecast

## Slide 21: Great Lakes Nearshore and Coastal Systems Climate change impacts will directly affect the physical integrity of the Great Lakes coastal and nearshore systems, which will in turn affect the Great Lakes habitats and the ecosystem
Seasonal Changes in Water Level Regimes and Storm Frequency:
  Slightly lower mean average water levels and increased water level variability – Increased potential for coastal and riverine flooding, altered coastal wetland biodiversity, loss of connectivity or inundation of coastal and riparian spawning/nursery habitats, altered marina/harbor/port access (increase dredging activity). A – high, C - >66%
  Increased Storm magnitude and Frequency - Altered littoral sediment transport processes, increased shore erosion, reduced nearshore water quality, reduced marina/harbor/port access (increase dredging activity), declining open-lake spawning fish recruitment. A – high, C – >95% (medium low and 33-66% for fish recruitment)
Seasonal Changes in Precipitation
  Increased spring-summer flows and runoff – Increased flows/nutrient loading promotes nearshore algal blooms, changes in seasonal flood-pulse driven spawning activity (recent Lake Erie example) A – high, C – >95% (for shallow lakes, but scale and timing issues for deep lakes <33%)
Altered Thermal Regimes:
  Higher surface water temperatures - Increased primary productivity (eutrophication) and changes in seasonal timing (spawning initiated earlier/later due to thermal triggers) A - high, C - >66%
  Deeper and stronger thermocline - Reduced Lake Erie hypolimnion volume and expansion of central basin hypoxia (bottom waters) A – medium high, C – 33-66% (linked to productivity, water levels)
  Change in species distributions - Boundaries for up to 19 fish species would shift northward (both cold and warmwater species) A – medium high, C – 33-66%
  Lower thermal constraints – Expansion of invasive species (both wetland and aquatic) A- medium low, C - >66%